## Slide 1: Progress towards Fusion Energy at ITER
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.
D.J. Campbell
ITER Organization, Route de Vinon sur Verdon, CS90 046, 13067 St Paul-lez-Durance, France
Acknowledgements:
Many colleagues in the ITER Organization, Domestic Agencies, ITPA and the international fusion programme

## Slide 2
ITER is a major international collaboration in fusion energy research involving China, the EU (plus Switzerland), India, Japan, the Russian Federation, South Korea and the United States
The overall programmatic objective:
  to demonstrate the scientific and technological feasibility of fusion energy for peaceful purposes
The principal goal:
  to design, construct and operate a tokamak experiment at a scale which satisfies this objective
ITER is designed to confine a DT plasma in which -particle heating dominates all other forms of plasma heating:
   a burning plasma experiment
What is ITER?

## Slide 3: The ITER Mission
ITER tokamak
ITER Program Objective:
  to demonstrate the scientific and technological feasibility of fusion energy for peaceful purposes
Key Technical Goals:
  achieve extended burn of a DT plasma with dominant alpha-particle heating (Q ≥ 10, ~500 s)
  develop steady-state fusion power production as ultimate goal
  integrate and test all essential fusion power reactor technologies and components
  demonstrate safety and environmental acceptability of fusion

## Slide 4: The ITER Tokamak
R=6 m
h=29 m
Be
W

## Slide 5
Fusion power production in ITER: the physics basis
ITER construction status
The ITER Research Plan
Elements of ITER physics and technology research
Synopsis
Notes: THE objectives set out for ITER are basically two:
ONE: to obtain and study a plasma where the alfa particle heating is dominating all other forms of heating.
ITER will operate with a value of capital Q greater than 10.
The fusion power in ITER will be about 500MW, the input power about 50MW.
And TWO: it has to integrate the technology required for future use of fusion as an energy source

## Slide 6
Temperature - Ti: 1-2 108 K (10-20 keV) (~10  temperature of sun’s core)
Density - ni: 1 1020 m-3 (~10-6 of atmospheric particle density)
Energy confinement time - E: few seconds ( current  radius2) (plasma pulse duration ~1000s)
Fusion power amplification: Present devices: Q ≤ 1
 ITER: Q ≥ 10
’Controlled ignition’: Q ≥ 30
Plasma fusion performance

## Slide 7
th  IpR2P-2/3
Turbulent transport in fusion plasmas difficult to predict quantitatively:
  so, we use scaling experiments to predict the level of energy confinement in ITER
  H-mode turns out to be robust enough to provide the basis for the ITER design  significant reduction in size of device
Plasma Confinement: tE Scaling
Plasma Current
Major Radius
Input Power

## Slide 8
ITER Plasma:
R/a: 6.2 m /2 m
Volume: 830 m3
Plasma Current: 15 MA
Toroidal field: 5.3 T
Density: 1020 m- 3
Peak Temperature: 2108 K
Fusion Power: 500 MW
Plasma Burn 300 - 500 s
(“Steady-state” ~3000 s)
D2,T2 Fuel
D++T+
He++(3.5MeV)
n(14.1MeV)
Blanket: neutron absorber
Power Plant
Li-->T
High temperature
He, D2,T2, impurities
Divertor: particle and heat exhaust
ITER: fusion power production

## Slide 9: ITER is making a successful transition from detailed design to construction
Large scale prototyping of major components is preparing the ground for series manufacture
Significant manufacturing activities and construction work are already underway in several critical path areas
In November 2012, the French Government authorized the creation of the installation nucléaire de base ITER
Substantial expansion of on-site construction activities is planned in the coming months

## Slide 10
ITER – Tokamak Core Components
Central Solenoid (6) (Nb3Sn)
Toroidal Field Coils (18) (Nb3Sn)
Cryostat (SS)
Shielding Blanket Modules (SS/ Be)
Thermal Shield (SS)
Correction Coils (18)
(NbTi)
Internal Coils
(Cu)
Poloidal Field Coils (6) (NbTi)
Vacuum Vessel (SS)
Divertor (SS/ W)
h ~ 29 m
d ~ 30 m

## Slide 11
IC
Ion Cyclotron 40-55MHz
20MW* +20MW#
Sawtooth control modulation < 1 kHz
LH
Lower Hybrid ~5 GHz
0MW* +40MW#
Off-axis bulk current drive
EC
Electron Cyclotron 170GHz
20MW* +20MW#
NTM/sawtooth control modulation up to 5 kHz
*Baseline Power
#Possible Upgrade
NB
Neutral Beam - 1 MeV
33MW* +16.5MW#
Bulk current drive limited modulation
ITER heating and current drive systems

## Slide 12
About 40 large scale diagnostic systems are foreseen:
  Diagnostics required for protection, control and physics studies
  Measurements from DC to -rays, neutrons, -particles, plasma species
  Diagnostic Neutral Beam for active spectroscopy (CXRS, MSE ….)
UPPER PORT
(12 used)
EQUATORIAL PORT
(6 used)
DIVERTOR PORT
(6 used)
DIVERTOR CASSETTES
(16 used)
VESSEL WALL
(Distributed Systems)
Analyzing the Plasma - ITER Diagnostics

## Slide 13
90% of ITER components will be supplied “in-kind” by the Members through their Domestic Agencies
ITER – A Major International Collaboration
*
This approach necessitates the integration of ITER management, design and procurement activities across the globe
Notes: 13

## Slide 14
Conductor
China
South Korea
Japan
Russia
United States
Europe
TF Coil
Japan
TF coil cases
Japan
Europe
TF Coils – A Global Collaboration

## Slide 15
TF Qualification Sample Summary
All TF conductor qualification samples were manufactured at CRPP and enabled supplier qualification in all 6 DAs involved in TF conductor production
Currently, virtually all of required >500t of Nb3Sn strand has been produced around the world
TF Strand Production Summary
TF Conductor Production

## Slide 16
Vacuum Vessel Manufacturing Contracts Awarded
VV sector, port and in-wall shielding PAs signed (EU, KO, RF, IN)
  industrial contracts awarded in each area by corresponding DA
Vacuum Vessel is a double-walled stainless steel structure
  19.4m outer diameter, 11.3m height, 5300 tonnes
  provides primary tritium confinement barrier

## Slide 17
Welding of Centering Keys and Inter-Modular Keys
Port Stub
R&D for IVC Rail Support
ITER Vacuum Vessel Prototyping
Fabrication of Upper Segment (PS2)

## Slide 18
Top Lid
Upper Cylinder
Lower Cylinder
Base Section
IN-DA signed PA September 2011
Contract awarded in August 2012
304L Stainless steel 40 – 180 mm thick
Diameter: 29.4 m/ Height: 29 m
Weight ~3500 tonnes
Base pressure < 10-4 mbar
Transfers loads to tokamak complex floor
Cryostat
Notes: 18

## Slide 19
40° Prototype Cryostat Base Section
Cryostat pedestal ring- bottom plate (180 mm & side plates (120 & 80 mm thick being welded
Cryostat pedestal ring- top plate 200 mm and skirt plate 105 mm thick welded together
Notes: 19

## Slide 20: Aerial views of platform – April 2014
Tokamak Complex
PF Coil Winding Building
Cryostat Workshop (IN)
ITER Construction at St Paul-lez-Durance
ITER Headquarters
400 keV Substation

## Slide 21
PF Coil Winding Building
Tokamak Complex Construction with new ITER HQ Building
Tokamak Complex Seismic Piles
Cryostat Workshop
Tokamak Complex Concrete Pour
ITER Construction at St Paul-lez-Durance

## Slide 22
Construction of Assembly Hall begins
B2 slab complete and cranes in place for Tokamak Complex construction
ITER Construction at St-Paul-lez-Durance

## Slide 23
POWER SUPPLIES
TOKAMAK BUILDING
OFFICE BUILDING
39 buildings and technical areas, 180 hectares
ITER Site Overview (~2020)

## Slide 24
ITER Research Plan – Rationale
The ITER Research Plan has been developed to analyze the programme towards high fusion gain DT operation:
  allows programme logic to be developed and key operational challenges to be identified and addressed during ITER construction
  supports planning of installation and upgrade programme accompanying operation
  provides insight into principal physics risks impacting on experimental programme  R&D priorities in current research programmes
  encourages exploration of issues in burning plasma physics which are likely to be encountered on route to Q = 10 and beyond

## Slide 25
ITER Research Plan – Structure
Hydrogen/ Helium
Develop plasma scenarios
Commission Control, H&CD, Diagnostics
Disruptions, Disruption Mitigation
H-modes (helium)
ELM control
Deuterium
Deuterium H-modes
DT scenario preparation
Trace tritium experiments
DT
Fusion power production
Q=10
Towards long pulse
more DT
Towards the future
0
1
2
3
4
5
6
7
8
9
10
INT TBM
EM-TBM
TN-TBM
NT/TM-TBM
TBM Program

## Slide 26
Research Plan Structure and Activities
Non-active operation:
  plasma operation to ~3.5 MA to establish initial divertor operation
  disruption loads, disruption detection, avoidance and mitigation
  development of plasma operation to ~7.5 MA/ 2.65 T
  H-mode operation and ELM Control
  demonstration of 15 MA/ 5.3 T operation
Nuclear operation:
  development of deuterium H-modes and preparation of DT scenarios
  initial DT operation to short-pulse Q=10
Subsequently, long-pulse Q=10 scenarios and ‘advanced’ operational scenarios will be developed, including non-inductive steady-state operation

## Slide 27
Top 12 risks associated with plasma operation and their potential consequences have been identified; mitigation strategies (and implications) have been developed – top 6 are:
  Disruption loads and effectiveness of disruption mitigation
  Uncertainty in H-mode power threshold scaling
  Effectiveness of ELM mitigation schemes
  Vertical stability control limited by excessive noise (or failure of in-vessel coils)
  Availability of reliable high power heating during non-active phase of programme ( H-mode access)
  Acceptable “divertor” performance with tungsten PFCs over required range of plasma parameters
Risk Assessment  Key R&D Needs

## Slide 28
ITER reference plasma scenarios
The set of DT reference scenarios in ITER is specified via illustrative cases in the Project Requirements:
 Design Basis plasma scenarios

## Slide 29
A Q ≥ 10 scenario with:
Ip=15 MA, Paux=40 MW, Pfus~500 MW
Current Ramp-up Phase
100
200
300
400
500
600
Time (s)
P (MW), Q
5.0
6.0
7.0
8.0
R (m)
T (keV)
n (1019 m-3))
12
6
0
18
24
30
10
8
0
2
4
6
-40
40
80
120
0
ITER Plasma Scenario - ELMy H-mode

## Slide 30
Discovery of internal transport barriers  “advanced scenarios”
But development of an integrated plasma scenario satisfying all reactor-relevant requirements remains challenging
plasma with reversed central shear + sufficient rotational shear
internal transport barrier  enhanced confinement
reduced current operation + large bootstrap current fraction
reduced external current drive + current well aligned for mhd stability and confinement enhancement
active mhd control
Steady-state operation + High fusion power density
Steady-State Operation

## Slide 31
Burning plasma: self-heated by a-particles
  non-linearity in total heating power due to dependence on plasma profiles
  MHD: sawtooth stabilization by a-particles, fast particle modes
Plasma control (position, shape, fuelling, heating, stability, exhaust)
  time constant for position control is >1s ⇒ very easy to damage plasma-facing components (e.g. on inner wall of vacuum chamber)
  very complex control matrix
Very high stored energy
  disruptions, ELMs, melting of metallic PFCs
High plasma current (15 MA for Baseline Q = 10 scenario)
  runaway electron damage of PFCs, huge disruption forces
High ion fluence (integrated plasma flux) to PFCs
  erosion of PFCs and migration of wall material, dust formation
What’s different about ITER physics and operation ?

## Slide 32
Since the establishment of the ITER Baseline in July 2010, the ITER project has moved fully into the Construction Phase
  on-site construction of the Tokamak Complex is underway
  Domestic Agencies have launched large scale manufacturing contracts for many major components
  extensive prototyping is ongoing in preparation for series manufacture
  there has been substantial progress in design and R&D for In-Vessel Components, Plasma Auxiliary Systems, Remote Handling, TBM etc
ITER Organization has been authorized to establish the installation nucléaire de base ITER
An extensive international collaboration is active in pursuing physics R&D for ITER in support of the preparations for ITER operation
Successful exploitation of ITER will realize the limitless possibilities of fusion energy, and open new areas of research in fusion plasma physics and fusion technology, including tritium breeding
Conclusions

## Slide 33
Thank you for your attention

## Slide 34
Backup Slides

## Slide 35
A magnetically confined plasma is a complex state
  it cannot be created and sustained without a sophisticated feedback control system
Free energy which is available within the plasma tends to generate turbulence and magnetohydrodynamic instabilities (mhd) which reduce plasma confinement quality
  great effort is expended within plasma control to sustain a high quality plasma capable of producing significant fusion power
In a thermonuclear plasma with significant fusion power, additional control requirements are imposed in ensuring the fusion power can be sustained for extended periods
  failures of the control system lead to conditions which tend to reduce fusion power or extinguish the plasma
At this stage of R&D, significant (uncontrolled) excursions in fusion power appear unlikely (ie burn point is stable)
  measures exist to control and suppress such excursions
Plasma Control

## Slide 36
Measurements: >50 systems thousands of data channels
Actuators: Magnets, Heating and current drive systems, Fuelling and pumping ~20 in total
Plasma Control System (PCS) ~20 parameters controlled simultaneously timescales from 1 ms to several seconds (blink of an eye ~50-80 ms) Requires state of the art control schemes
Ensure that physics objectives of any discharge are met
Provide first level of machine protection (other levels above)
Plasma Control on ITER
Notes: Neural network = réseau de neurones si tu veux faire “le bon français qui traduit tout”
Application programming = interface de programmation

## Slide 37
TBM
TBM ports
n + 6Li  T + 4He + 4.8MeV
n + 7Li  T + 4He + n - 2.47MeV
Three dedicated stations for testing up to six tritium breeding concepts
Test Blanket Modules - Tritium Breeding
TBM Port Plug (exploded view)

## Slide 38: Component transport
For heaviest components: vacuum vessel sectors, toroidal field coils, poloidal field coil 1 and 6 Road upgrades from south coast to Cadarache complete and paid for by regional funding (115 M€) ITER itinerary ~104 km by road + 32 km by barge
Component Transport

## Slide 39
352 wheel test convoy carrying 800 ton load (33 m long, 9 m wide, 10 m high) trialled in September 2013 and March/April 2014
  2 power generators developing 730 horse power
Component Transport
Crossing Etang de Berre (32 km)
Journey lasts 4 nights